## Slide 1
Joystick-Controlled Robot Car
Using HCS12 Microcontroller & MATLAB Simulink
Tasneem Barakat • Malak Alhajaj • Renad Al-Nimat
January 2026

## Slide 2
Agenda
01
Project Overview
Goals and objectives
02
System Architecture
Master-slave design
03
Hardware Components
HCS12, Arduino, L298N
04
HCS12 Software
ADC, Serial, Control logic
05
Simulink Model
Model-based motor control
06
Problems & Solutions
Challenges faced
07
Conclusion
Key takeaways

## Slide 3
Project Overview
Project Goal
Build a joystick-controlled 4WD robot car demonstrating embedded systems integration
Our Approach
HCS12 for control logic + Arduino with Simulink model-based design for motor control
Key Objectives
Hands-on experience with HCS12 microcontroller (automotive applications)
Implement ADC for joystick reading and serial communication
PWM-based motor speed control with H-bridge driver
Model-based design using MATLAB Simulink for Arduino

## Slide 4
System Architecture
Joystick
Analog X/Y
→
HCS12
MASTER
ADC + Logic
7-Seg Display
→
Serial
9600 baud
Arduino
SLAVE
Simulink Model
PWM Control
→
L298N
H-Bridge
Command Protocol
Command | ASCII | Decimal | Action | Display
'F' | 0x46 | 70 | Forward | 4
'B' | 0x42 | 66 | Backward | 3
'L' | 0x4C | 76 | Left | 1
'R' | 0x52 | 82 | Right | 2
'S' | 0x53 | 83 | Stop | 0

## Slide 5
Hardware Components
Dragon12-JR
MC9S12DG256
16-bit HCS12 core
256KB Flash, 12KB RAM
4 MHz bus clock
10-bit ADC (ATD1)
7-segment display
Analog Joystick
2-Axis Input
X-axis: center ~550
Y-axis: center ~150
Left threshold: 350
Right threshold: 750
Push button backup
Arduino Uno
ATmega328P
16 MHz clock
Simulink deployed
Serial receive (Port 0)
PWM pins 5, 6
Digital pins 8,9,10,11
L298N H-Bridge
Dual Motor Driver
Channel A: Left motors
Channel B: Right motors
ENA/ENB: Speed (PWM)
IN1-IN4: Direction
7-12V motor supply

## Slide 6
HCS12 Controller Software
Key Software Functions
ADC Initialization
ATD1CTL2 = 0x80 (power up)
ADC Read
10-bit conversion on PAD8/PAD9
Serial Init
SCI1BDL = 26 (9600 baud @ 4MHz)
Serial Send
Wait TDRE flag, write to SCI1DRL
Button Check
PA0 active-low with pull-up
7-Seg Display
Port H, common-anode (inverted)
Command Logic
char get_command(x, y) {
if(button_pressed())
return 'B';
if(x <= 350) return 'L';
if(x >= 750) return 'R';
if(y >= 350) return 'F';
return 'S';
}
Joystick Calibration
X center: ~550 | Y center: ~150
Y-axis broken → Push button for backward

## Slide 7
MATLAB Simulink Model-Based Design
Why Model-Based Design?
Visual block-based design
Simulate before deploying
Auto code generation
No hand-written Arduino code
Easy to modify and debug
Simulink Blocks Used
Block Type | Qty
Serial Receive | 1
Constants | 7
Relational Operators | 5
OR Gates | 5
Data Converters | 4
Switches | 2
Digital Output | 4
PWM | 2
Direction Logic (OR Gates)
IN1 = isForward OR isRight (left motor forward)
IN2 = isBackward OR isLeft (left motor backward)
IN3 = isForward OR isLeft (right motor forward)
IN4 = isBackward OR isRight (right motor backward)
Enable = F OR B OR L OR R (movement active)

## Slide 8
Motor Control Logic
Arduino to L298N Wiring
Arduino | L298N | Function
Pin 8 | IN1 | Left direction
Pin 9 | IN2 | Left direction
Pin 11 | IN3 | Right direction
Pin 10 | IN4 | Right direction
Pin 6 | ENA | Left speed (PWM)
Pin 5 | ENB | Right speed (PWM)
Motor Control Truth Table
Move | IN1 | IN2 | IN3 | IN4 | PWM
Forward | 1 | 0 | 1 | 0 | 80
Backward | 0 | 1 | 0 | 1 | 80
Left | 0 | 1 | 1 | 0 | 80
Right | 1 | 0 | 0 | 1 | 80
Stop | 0 | 0 | 0 | 0 | 0
Deployment Process
1
Design model in Simulink
2
Configure for Arduino Uno
3
Build, Deploy & Start
4
Auto-generates C code

## Slide 9
Problems & Solutions
Problem | Symptom | Solution
Wrong serial pin | No data received | Use PS3 (TX), not PS2 (RX)
Wrong baud rate | Garbage characters | SCI1BDL = 26 for 4MHz bus
Joystick Y-axis broken | No backward movement | Added push button on PA0
Motors going in circles | Car not going straight | Fixed motor wiring polarity
Non-PWM pin used | Motor always full speed | Use PWM pins (5, 6)
Key Lessons Learned
Always verify pin assignments from datasheets before wiring
Hardware problems can often be solved in software
Systematic testing saves debugging time

## Slide 10
Conclusion
Successfully integrated HCS12 + Arduino + Simulink
Implemented 5 movement commands (F/B/L/R/S)
Model-based design eliminated hand-written Arduino code
Visual feedback via 7-segment display
Learned to adapt: software fixes for hardware issues
Future Improvements
Wireless communication • Obstacle avoidance • Proportional speed control • Camera integration

## Slide 11
Thank You!
Questions?
Tasneem Barakat • Malak Alhajaj • Renad Al-Nimat
January 2026